ALSA Sound system
Martin Stransky
stransky@redhat.com

---
Agenda
Sound card architecture
ALSA Sound System architecture
High-level components
  1. ALSA plug-ins
  1. ALSA configuration
  1. ALSA API
Mixer interface

---
Sound architecture (1)
raw pcm data
PCI
raw buffer
raw pcm data
raw pcm data
D/A
LP
analog output
system memory
sound card

---
Sound architecture (2)
system memory (user data to play)
CPU
DMA
PCI bus
IRQ
sound card

---
ALSA Sound system
A glue between user-space application and low-level card driver
alsa-lib
alsa core
application
card driver
/proc
user space
kernel space

---
ALSA Sound system – card driver
Manages low-level card access (via I/O ports)
  1. Card set-up (initialization, shut-down)
  1. Card configuration
  1. Low-level PCM playback
    1. DMA set
    1. IRQ set / interupt routines
    1. Routines for start / stop playback / record
  1. Low-level mixer routines, read / write actual control settings
alsa-lib
alsa core
card driver
user space
kernel space

---
ALSA Sound system – alsa core
Manages buffers with sound data
  1. Menory management
    1. Buffers, control structures
  1. Transfer data from / to userspace
  1. Export mixer interface to userspace
Manages timers & synchronization
alsa-lib
alsa core
card driver
user space
kernel space

---
ALSA Sound system – alsa-lib
Sound plug-ins
  1. dmix, dsnoop, file, plug
Manages sound & plug-in configuration
  1. Default sound card and device
  1. Configuration for specified cards
Provide API for alsa core
alsa-lib
alsa core
card driver
user space
kernel space

---
ALSA Sound system – application
Only uses alsa-lib API
  1. Need to prepare data in supported formats
    1. Proper sample rate / bits / channels
  1. Loading / storing data from / to disc
  1. Configure plug-ins, mixer settings and so on...
alsa-lib
alsa core
card driver
user space
kernel space

---
High-level components - ALSA plug-ins
Part of alsa-lib so it’s a part of application
user space
kernel space
alsa-lib
alsa core
card driver
plug
hw
route &
volume
alsa core
driver
plug
hw

---
ALSA plug-in - dmix
Software mixer for playback
Uses shared memory and semaphores
Used only with cards w/o HW mixer
dmix
dmix
hw
alsa core
driver
dmix

---
ALSA plug-in - dsnoop
Software mixer recording
Reverse way of dmix plugin
dsnoop
driver
alsa core
hw
dsnoop
dsnoop

---
ALSA plug-ins
HW – access to sound card, playback, record
Plug – converts format of samples (rate, bits), channel routing
File – writes PCM stream to disk
Route & Volume – software volume and channel routing (stero to 5.1...)
Multi – converts multiple PCM streams to one multi-channel stream
Asym – can connects dmix and dsnoop to one full-duplex device
alsa core
driver
plug
hw

---
ALSA configuration – hw plug-in
 hw:0,0 – Stereo capture / playback
 hw:0,1 – Multichannel playback
hw:0
 hw:0,2 - IEC958
hw:1
 hw:1,0 – Stereo capture / playback

---
ALSA configuration – hw plug-in
hw
aplay -D hw:0,1 sample.wav
Plug-in - hw
Card - 0
Device - 1
dmix
hw
aplay -D dmix sample.wav

---
ALSA configuration - “default” plug-in
default
hw
aplay sample.wav
/etc/asound.conf
~/.asoundrc
pcm.!default {
type hw
card 0
}
ctl.!default {
type hw
card 0
}

---
ALSA configuration – all plug-ins
It’s readed by alsa-lib
Plug-in parameters,
Main configuration in /etc/alsa/alsa.conf, includes:
  1. /etc/asound.conf, ~/.asoundrc
  1. /etc/alsa/cards/*.conf for specified card (by driver name)
  1. /etc/alsa/pcm for pre-defined plug-ins (dmix, dsnoop, default)
pcm.NAME {
    type hw # Slave PCM plug-in
     card INT/STR # Card name or number
     [device] INT # Device number (default 0)
...	# Next params
}
pcm.my_device {
    type hw
     card 0
     device 0
}

---
ALSA configuration – plug-in usage
aplay -D pcm.my_device sound.vaw
pcm.my_device {
    type hw
     card 0
     device 0
}
cards.pcm.default:0
cards.EMU10K1.pcm.front.0:0

---
API interface
snd_pcm_open(pcm_handle, Name, Stream, Mode)
  1. pcm_handle – new pcm handle
  1. Name – name of plug-in (“hw”, “default”...)
  1. Stream – record / playback
  1. Mode – block / non-block access
snd_pcm_hw_params
  1. access, format, channels, periods, buffer_size
snd_pcm_writei(pcm_handle, buffer, size) / snd_pcm_readi (pcm_handle, buffer, size)
  1. pcm_handle – handle of pcm stream (first access starts playback / record)
  1. buffer – data to playback / space for record
  1. size – frames to play / record (frame = one sample for all channels)

---
Mixer interface
The weakest part of ALSA architecture
Only exports controls from card to user-space
R2
R5
USB
R1
D/A
A/D
R4
DOUT
DIN
R3
A2
A3
SPK
LIN
A1
D1
USB

---
Troubleshooting
“aplay -l” - list of all cards in system
“aplay -L” - list all PCM devices
/proc/asound/* - general info, loaded modules, card types...
“alsamixer” - low-level set-up

---
Reference
http://www.alsa-project.org
http://www.alsa-project.org/documentation.php
http://www.alsa-project.org/alsa-doc/doc-php/asoundrc.php
http://www.suse.de/~mana/alsa090_howto.html
http://www.alsa-project.org/~iwai/writing-an-alsa-driver/index.html